## Slide 1: Dynamic Erase Voltage and Time Scaling for Extending Lifetime of NAND Flash-Based SSDs
2017.08.02
DC Lab
서영근
Distributed Computing Laboratory in SKKU

## Slide 2: Content
Introduction
NAND Flash Memory
Erase Voltage and Time Scaling
Write Capability Tuning
Design and Implementation of dvsFTL
Experimental Results
Distributed Computing Laboratory in SKKU

## Slide 3: Introduction
NAND Endurance
  ability of a memory cell to endure program/erase (P/E) cycling
  기술이 발전 함에 따라 NAND Endurance 가 하락하고 있다.
  이는 NAND 플래시 Lifetime의 증가를 막는 아주 중요한 문제
NAND Endurance 를 증가 시키는 두 가지 방법
  Lower erase voltage로 erase하기
  느리게 지우기 (slowly erasing)
Distributed Computing Laboratory in SKKU

## Slide 4: Introduction
DeVTS
  Dynamic Erase Voltage and Time Scaling
  -> 본 논문에서 제시하는 방법
  Idea : NAND Endurance 감소가 erase 과정에서
  일어난다는 것에서 시작했다.
  -> 산화물 손상 (oxide damage)
  NAND 플래시 소프트웨어에 여러 가지 erase
  scale을 고를 수 있게 한다면 성능을 높일 수 있을 것
  -> 적은 전압으로 지우기
  여기서 문제가 생기는데 지울 때 적은 voltage로
  지우면 쓸 때 스페셜한 write 모드가 필요하다.
  -> threshold voltage의 간격 조절
  -> time scale 조절
Distributed Computing Laboratory in SKKU

## Slide 5: NAND Flash Memory
NAND Flash Memory design (논문에서 MLC 위주로 설명)
  2개의 비트를 4가지의 전압상태로 정보를 셀에 저장하는 memory
  WVth 와 NAND endurance 는 반비례 관계이다.
  WVth가 길어지면 w 와 m 도 자연스럽게 길어져 performance가 좋아지지만, NAND endurance는 낮아진다. (Deeply erased)
  NAND endurance를 올리기 위해 WVth을 줄일 때 어떠한 방식으로 margin 과 width를 줄 지가 이 논문의 주제
Distributed Computing Laboratory in SKKU

## Slide 6: Erase Voltage and Time Scaling
Erase Voltage Scaling and Its Effect on Endurance
  Retention BER : the number of retention errors divided by the total number of tested cells
  Effective wearing : The effective degree of NAND damage after one P/E cycle.
Distributed Computing Laboratory in SKKU

## Slide 7: Erase Voltage and Time Scaling
Erase Time Scaling and Its Effect on Endurance
Distributed Computing Laboratory in SKKU

## Slide 8: Write Capability Tuning
Write Performance Tuning
Distributed Computing Laboratory in SKKU

## Slide 9: Write Capability Tuning
Retention Capability Tuning
  NAND flash memory is required to retain its stored data for the specified retention time
  그러나 이 값을 조정하면 Margin 넓이를 줄일 수 있다.
  Short retention time write 와 long retention time write를 구분할 수 있을 것
Distributed Computing Laboratory in SKKU

## Slide 10: Write Capability Tuning
4가지 튜닝을 정리
  지금 까지 설명한 4가지 튜닝 (erase voltage,
  Erase time(speed), write speed,
  write retention) 을 하나의 표로 정리한 것.
  EVmode0 이 가장 높은 voltage이고
  EVmode5가 가장 낮은 voltage이다.
  Erase speed 는 2가지, write speed는 3가지로
  분류하며, write retention mode는 2가지이다.
Distributed Computing Laboratory in SKKU

## Slide 11: Design and Implementation of dvsFTL
overview
  Write speed,
  Erase speed(buffer)
  Write mode
  (retention time
  predictor)
  Erase voltage
Distributed Computing Laboratory in SKKU

## Slide 12: Design and Implementation of dvsFTL
Write-Speed Mode Selection
  Write speed(buffer)
  Erase speed 도 비슷한 개념
Distributed Computing Laboratory in SKKU

## Slide 13: Design and Implementation of dvsFTL
Write-Retention Mode Selection
Distributed Computing Laboratory in SKKU

## Slide 14: Experimental Results
NAND Lifetime Analysis
Distributed Computing Laboratory in SKKU

## Slide 15: Experimental Results
Overall Write-Performance Requirement
Distributed Computing Laboratory in SKKU

## Slide 16: 감사합니다
Distributed Computing Laboratory in SKKU