## Slide 1: Amnesic Cache Management for Non-Volatile Memory
2017.07.02
DC Lab
서영근
Distributed Computing Laboratory in SKKU

## Slide 2: Content
Introduction & motivation
Design
  REF
  SACM
  AACM
Evaluation
Conclusion
Distributed Computing Laboratory in SKKU

## Slide 3: Introduction & motivation
Non-Volatile Memory
  PCM (Phase Change Memory), STT-RAM (Spin Transfer Torque RAM), ReRAM (Resistive RAM), Fe-RAM (Ferroelectric Random Access Memory)
  Byte addressability and Non-Volatility
  Limited retention capability, relaxation write
    결국 비휘발성의 특징도 매우 장기적인 시각에서 휘발성이라는 뜻
Distributed Computing Laboratory in SKKU

## Slide 4: Introduction & motivation
PCM (Phase Change Memory)
  target band : A region of resistances that corresponds to valid bits
  margin : between target band and boundary
  resistance drift
    The resistance in a PCM cell has a tendency to increase by time
    When the resistance drifts up to the boundary of the next region, the state can be incorrectly represented leading to data loss
Distributed Computing Laboratory in SKKU

## Slide 5: Introduction & motivation
Tradeoff between retention capability and write speed
  target band 를 줄이면 resistance drift 가능성이 줄지만 그 만큼 margin이 늘어나 write latency가 늘어난다.
  Higher retention increasing write latency
Distributed Computing Laboratory in SKKU

## Slide 6: Introduction & motivation
NVM cache
  Fetching/Eviction data from/to storage system
  Retention capability for the cache
    10⁷ seconds is recommended retention capability from JEDEC
    But, data will be evicted from the NVM cache
Distributed Computing Laboratory in SKKU

## Slide 7: Introduction & motivation
Caching time
  T(caching) = T(evict) −T(first)
  75% of the data is less than 10⁵ seconds
  Don’t need to ensure 10⁷ seconds retention capability in the cache
Distributed Computing Laboratory in SKKU

## Slide 8: Introduction & motivation
retention capability 을 낮춰서 Write Performance를 Improve 할 수 있는 cache를 제안
Distributed Computing Laboratory in SKKU

## Slide 9: Design - REF
REF(REFresh-based cache management scheme)
  REF is similar to the LRU scheme
  Higher retention increasing write latency
  Enhances write speed by relaxing retention capability from 10⁷ to 10⁴
  Problem
    Refresh operation, additional write
Distributed Computing Laboratory in SKKU

## Slide 10: Design - SACM
Simple Amnesic Cache Management
  Free State to Tentative State
    Initial write into the cache, the data is written with the relaxed write(10⁴)
  Tentative State to Confirmed State
    If it is referenced again within the retention time
    It is rewritten with 10⁷ retention capability
  Confirmed State to Free State
    If it is not referenced again and
    the retention time expires
  Problem
    Additional writes
Distributed Computing Laboratory in SKKU

## Slide 11: Design - AACM
Adaptive Amnesic Cache Management
  Estimates the next reference of each data and adaptive write
  Adaptive write
    Ensure appropriate retention capability adaptively for each data
  Problem
    Adaptive write and Estimation
Distributed Computing Laboratory in SKKU

## Slide 12: Evaluation
latency
  REF reduces 48% (36% on average)
  SACM 7% (4% on average)
  AACM does it up to 40% (30% on average)
Distributed Computing Laboratory in SKKU

## Slide 13: Evaluation
Energy consumption
  REF is 9 times higher than LRU (refresh overhead)
Distributed Computing Laboratory in SKKU

## Slide 14: Evaluation
Energy consumption (without REF)
  SACM reduces energy consumption on average 11%
  AACM saves energy consumption on average 37% (and as high as 49%)
Distributed Computing Laboratory in SKKU

## Slide 15: Conclusion
Conclusion
  We suggest “Amnesic notion”
  Exploit limited retention capability
  Experimental results show that our proposal is effective in terms of
  performance and energy consumption.
    AACM can reduce write latency by up to 40% (30% on average)
    Also, AACM save energy consumption by up to 49% (37% on average)
Distributed Computing Laboratory in SKKU

## Slide 16: 감사합니다
Distributed Computing Laboratory in SKKU