## Slide 1: Parity-Stream Separation and SLC/MLC Convertible Programming for Lifespan and Performance Improvement of SSD RAIDs
Yoohyuk Lim, Jaemin Lee, Cassiano Campes, Euiseong Seo
yoohyuk.lim@csl.skku.edu
Sungkyunkwan University
The 9th USENIX Workshop on Hot Topics in Storage and File Systems (HotStorage’17)

## Slide 2: Introduction
In data centers or enterprise systems, SSDs are mostly used in a form of RAID for reliability and performance
In RAID-4, 5 and 6, parity bits are used for reliability
  Corresponding parity should be updated when data is updated
Access patterns of RAID reduce the lifespan of SSDs
  Because of partial stripe write
  Flash cells have limited life-cycle of write (program) and erase

## Slide 3: Partial Stripe Write Problem
RAID Controller
Parity
Data
Data
Data
Four SSDs with RAID
Three data blocks and one parity block in one stripe
Parity block in 4th SSD

## Slide 4: Partial Stripe Write Problem
RAID Controller
WR #1
WR #1
Parity
Data
Data
Data
WR #1
First write request requires updating the first data block
This induces update of corresponding parity block

## Slide 5: Partial Stripe Write Problem
RAID Controller
WR #1
WR #2
WR #1,2
Parity
Data
Data
Data
WR #1,2
Second write request requires updating second data block
The same parity block must be updated again

## Slide 6: Partial Stripe Write Problem
RAID Controller
WR #1
WR #2
WR #3
WR #1,2,3
Parity
Data
Data
Data
WR #1,2,3
For every write to this stripe, its parity block should be updated
This amplifies the number of write operations to the parity block

## Slide 7: Partial-Stripe Write Problem
To quantitatively verify write amplification from partial-stripe write
  We carried out FIO microbenchmark and measured number of writes to each disk
  Random writes smaller than stripe size
  Seven SSDs with RAID-4 (to fix parity disk)
5.3×

## Slide 8: Adversary Effect from Mixing Parity and Data
Block #1
Block #2
Block #3
…
SSD
RAID Controller
…
In RAID-5, 6, parity disk is rotated
Parity and data writes tend to interleave
Parity #1
Data #4
Parity #2
Parity #1
Parity #1
Data #2
Parity #2
Data #3
Data #3
Parity #7
Data #11
Parity #1
Parity #7
Data #5
Parity #1
Parity #7
Data #3
Valid page copy in garbage collection
Reduce lifespan and latency

## Slide 9: Our Approach to Reduce Parity-Induced Wear
Parity-stream separation
  Separate frequently-updating parity pages from data pages
  This reduces valid page copy operations during garbage collection
SLC/MLC convertible programming
  Various types of NAND flash memory
    Single-level Cell(SLC) and Multi-level Cell(MLC), etc
  SLC has a longer lifespan than MLC
  It is possible to program MLCs as if they are SLCs
  Our approach programs parity pages in SLC mode to extend lifespan

## Slide 10: Parity-stream separation
Separate flash blocks to parity blocks and data blocks
Reduce copy operations during garbage collection
Block #1
Block #2
Block #3
Parity
Parity
Parity
Data
Parity
Data
Data
Parity
Parity
Parity
Data
Parity
Parity
Data
Parity
Parity
Data
Parity
Data
Data
Data
Parity
Parity
Data
Block #1
Block #2
Block #3
Valid page copy during GC
Just free victim block

## Slide 11: Parity-stream separation
Multi-streamed SSDs
  Separate writing flash blocks according to stream IDs
  Assign stream IDs by life cycles of data
  Incorporated in NVMe 1.3 Specifications
21
20
1
100
Block #1
20
22
1
1
Block #2
1
1
Block #3
Without stream
1
1
20
1
22
1
21
100
20
1
Request data :
1
1
1
1
Block #1
20
21
20
22
Block #2
100
Block #3
Multi-stream
1
Block #4
Reduce valid pages to copy
Reduce GC overhead

## Slide 12: Parity-stream separation
RAID controller accordingly tags write requests with parity or data stream
SSD separately stores parity from data blocks
SSD
Parity Flash Blocks
Data
Data
Data
Data
Parity
Parity
Parity
Parity
Data Flash Blocks
Write Operation
Parity Stream
Data Stream
RAID-Controller

## Slide 13: SLC/MLC Convertible Programming
Separating parity and data blocks is not sufficient
  This reduces WAF caused by garbage collection
  However, it does not reduce the number of parity write operations itself
Reducing the wear caused by frequent parity writes is important
5.3×

## Slide 14: SLC/MLC Convertible Programming
SLC has a longer lifespan than MLC
SLC and MLC typically have the same structure
1
0
Single-level Cell
Vt
11
01
00
10
Multi-level Cell
Vt

## Slide 15: SLC/MLC Convertible Programming
SLC has a longer lifespan than MLC
SLC and MLC typically have the same structure
It is possible to change type of flash cells on demand
  To shorten write latency, some commercial MLC SSDs use a few of flash blocks as a write buffer simulating SLC
1
0
Single-level Cell
Vt
11
01
00
10
Multi-level Cell
Vt
SLC mode

## Slide 16: SLC/MLC Convertible Programming
Lifespan of SLC mode extends 7× more than MLC
Because SLC provides a half capacity in comparison to MLC, the endurance gain is 3.5× for the same amount of write operations
“Cactus Technologies, An overview of Pseudo-SLC NAND, White Paper, 2016”

## Slide 17: SLC/MLC Convertible Programming
Extend lifespan by allocating parity pages to SLC-mode blocks
  SLC blocks for parity block writes
  MLC blocks for data block writes
SSD
Parity
Parity
Parity Flash Blocks
SLC
Data
Data
Data
Data
Data Flash Blocks
MLC
Write Operation
Parity Stream
MLC
MLC
MLC
Free Blocks
Data Stream
RAID-Controller
FTL
SLC Allocation
MLC Allocation
SLC

## Slide 18: SLC/MLC Convertible Programming
Capacity shrinks when MLC blocks are used in SLC mode
  SLC block is half the size of MLC block
  Using MLC blocks as SLCs on demand may not guarantee the nameplated capacity
SLC
SLC
Capacity shrinks
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC

## Slide 19: SLC/MLC Convertible Programming
Capacity shrinks when MLC blocks are used in SLC mode
  SLC block is half the size of MLC block
  Using MLC blocks as SLCs on demand may not guarantee the nameplated capacity
Obtain extra blocks from over-provisioned area of SSDs
  Usually up to 28% of the nameplate capacity for enterprise SSDs
Over-provisioned area
Keep same capacity
SLC
SLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC

## Slide 20: SLC/MLC Convertible Programming
The number of available SLC blocks is limited according to the over-provisioned area size
  After reaching the upper limit, parity blocks will be allocated with MLC blocks
May increase the overhead of garbage collection
  Require to dynamically determine the optimal number of SLC blocks
Over-provisioned area
SLC
SLC
SLC
SLC
MLC|MLC
Maximum available SLC blocks
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC
MLC|MLC

## Slide 21: Evaluation Environment
RAID Controller in Linux
I/O with parity info
YCSB
Cassandra
TPC-C
MySQL
FIO
Block Layer
Block level I/O with parity info
Seven SSDs with RAID-5
Input
Simulation results
ftrace
FlashSim SSD simulator
Added tags to identify parity write
Added multi-stream, SLC/MLC convertible programming

## Slide 22: Parameters for SSD Simulator
Total block number |  | 2048
Over provisioned area |  | 28%
Page size |  | 16KB
No. of pages per block | SLC | 128
 | MLC | 256
Read delay | SLC | 20 us
 | MLC | 35 us
Write delay | SLC | 180 us
 | MLC | 390 us
Block erase latency |  | 4000 us
MLC:SLC write stress |  | 1.5×, 2.5×, 3.5×

## Slide 23: Parameters for SSD Simulator
Total block number |  | 2048
Over provisioned area |  | 28%
Page size |  | 16KB
No. of pages per block | SLC | 128
 | MLC | 256
Read delay | SLC | 20 us
 | MLC | 35 us
Write delay | SLC | 180 us
 | MLC | 390 us
Block erase latency |  | 4000 us
MLC:SLC write stress |  | 1.5×, 2.5×, 3.5×

## Slide 24: Reduced Page Copy Operations of Garbage Collection
When the number of page copy caused by GC is reduced, the response delays will be reduced as well
PS : Parity-stream
CP : SLC/MLC Convertible Programming
58%

## Slide 25: Reduced Page Copy Operations for Garbage Collection
When the number of page copy caused by GC is reduced, the response delays will be reduced as well
PS : Parity-stream
CP : SLC/MLC Convertible Programming
Cassandra
Copy-on-write database
Architecture is not appropriate for our scheme
Direct I/O
Buffered I/O

## Slide 26: Write Operation in Cassandra
Memory
Commit Log
Disk
Memtable
SSTable
Write Operation
SSTable
Immutable
SSTable
SSTable
Copy on write
Partial stripe writes are very small
Request large size of writes
No TRIM in the simulator
High capacity utilization
▶ Incapacitate parity separation

## Slide 27: Reduced Page Copy Operations for Garbage Collection
Convertible programming shrinks the over-provisioned area
▶Increase Garbage collection overhead
PS : Parity-stream
CP : SLC/MLC Convertible Programming
Most of copy operations in SLC mode
Performance decrease
< Copy operation increase
High capacity utilization due to COW and logging

## Slide 28: Expected Lifespans under Various MLC:SLC Stress
PS : Parity-stream
CP : SLC/MLC Convertible Programming
53%
Counted the number of write operations with write overhead
Assumed that MLC write stress has 1.5× ~ 3.5× of SLC’s

## Slide 29: Expected Lifespans under Various MLC:SLC Stress
PS : Parity-stream
CP : SLC/MLC Convertible Programming
Counted the number of write operations with write overhead
Assumed that MLC write stress has 1.5× ~ 3.5× of SLC’s
10%
The number of copy during GC was a relatively small portion of the total writes
The increased copy count barely affected lifespan

## Slide 30: Problem of SLC mode
Using SLC mode under condition of high capacity utilization
  Shrink the relative size of over-provisioned area
  Increase garbage collection overhead

## Slide 31: Overhead with Varying Capacity Utilization
FIO microbenchmark
Lines mean throughput, bars mean normalized lifespan
PS : Parity-stream
CP : SLC/MLC Convertible Programming
Storage capacity is being severely underutilized in most of data centers
No TRIM in the simulator
Our approach will operate under favorable conditions most of the time

## Slide 32: Overhead with Varying Capacity Utilization
Although diminishment of lifespan improvement occurred,
our approach extends lifespan of SSD in all conditions

## Slide 33: Overhead with Varying SLC Block Ratio
PS : Parity-stream
CP : SLC/MLC Convertible Programming
FIO microbenchmark
Each bar means capacity utilization
SLC Ratio 0% : Disable SLC mode of MLC blocks
SLC Ratio 100% : Enable all over-provisioned area to keep capacity

## Slide 34: Conclusion
We identified that partial stripe writes in RAID systems reduce the lifespan
We proposed the parity-stream separation and SLC/MLC convertible programming
Our evaluation showed that not only reduced garbage collection, but also improved lifespan of SSDs
Garbage collection can be further reduced when the parity-stream is split into multiple streams based on the update patterns

## Slide 35: Thank you
yoohyuk.lim@csl.skku.edu